## Slide 1: Predicting rock lithology using machine learning
Presented by:
Ovie Iboyitie
Predicting rock lithology using machine learning
Presented by:
Ovie Iboyitie
15th August, 2022

## Slide 2: Outline
Executive Summary
Introduction
Methodology
Results
Conclusion
Limitations and References

## Slide 3: Executive Summary
With the recent developments, computing power, and availability of large data, the use of machine learning approach has spurred the interest of the oil and gas industry. Other works have been done to predict lithology using machine learning. This approach uses deep neural networks to classify lithology using well logs, the location of the well, and its depth. The data was gotten from GitHub and wrangled. A model with an accuracy and f1 score of 0.89.

## Slide 4
Understanding reservoir lithology is the foundation from which all other petrophysical calculations are made. To make accurate petrophysical calculations of porosity, water saturation (Sw), and permeability, the various lithologies of the reservoir interval must be identified and their implications understood.
Obtaining a physical sample of the reservoir is the surest way to unambiguously determine lithology and rock type, but obtaining this physical sample is not always easy. Mud logs are the first choice in wildcat wells, but exact assignment of a rock fragment to a particular depth is not without error.
Introduction

## Slide 5
Methodology
DATA COLLECTION
DATA WRANGLING AND EXPLORATORY DATA ANALYSIS
MODEL DEVELOPMENT
MODEL EVALUATION
The data used for analysis was gotten from Github.
Create multiple models with different hyperparameters
.
Discover trends and issues with data
Evaluate several models based on several criterial and choose the best one
.

## Slide 6
Data Wrangling
  Duplicates were removed, and values for shallow resistivity, medium resistivity, deep resistivity, and photoelectric factor logs were dropped because removing outliers removes some classes. Outliers for density correction, gamma ray, neutron density, sonic (compressional slowness), and spontaneous potential logs were removed. Missing values were filled using an iterative imputer that predicts the missing value based on the values of the other columns for that observation

## Slide 7
EDA with Data Visualization
Shale is the most occurred lithology in the dataset and classes like Basement, halite, Coal, Chalk, dolomite, Anhydrite, marl, Tuff and Limestone are largely underrepresented. Hence, The classes are imbalanced

## Slide 8
EDA with Data Visualization
Gamma Ray, Spontaneous potential, and density correction logs are the three most independent well logs. The pairplot shows the relationship between two variables and the different lithologies

## Slide 9
EDA with Data Visualization
1.
3.
4.
2.
BS
CALI
DRHO
DTC

## Slide 10
EDA with Data Visualization
1.
3.
4.
2.
GR
NPHI
RHOB
SP

## Slide 11
Machine Learning Workflow
Model development
Develop the model to fit chosen architecture
Define Losses and Metrics
Train model on data
Model Evaluation
Evaluate Model on its accuracy, F1 score and jaccard score
Develop a neural network architecture
Hyperparameter tuning

## Slide 12
Model Architecture and Development
The Location (longitude and latitude), the depth, the NPD lithostratigraphy group, NPD lithostratigraphy formation, bulk density, raw gamma data, neutron density, sonic (compressional slowness), and spontaneous potential are used by the neural network to predict the lithology of the rock.
Model 1
Model 4
Model 3
Model 2

## Slide 13
Model Evaluation
Four models were developed using artificial neural network. Model 3 did better in predicting the lithologies with an accuracy of 0.89.
The model does very well in predicting nine lithologies with high precision and recall. It performs poorly on in predicting dolomite and halite.

## Slide 14: Conclusion
Using a deep neural network based on the multilayer perceptron, the rock lithologies were predicted, with accuracies up to 0.89. The model developed has a high recall and precision for predicting the other lithologies except for halite and dolomite and can be improved if more data are provided. The number of activation units and layers in the deep neural networks substantially affected the accuracy of the model. This model eliminated the cost or the need of going subsurface to acquire samples to determine rock lithology.

## Slide 15
Limitations and References
LIMITATIONS
1. Some logs that would probably have improved the predictions of the model had missing values over 50%. These logs include SGR, ROP, DTS, DCAL, MUDWEIGHT, RMIC, ROPA, RXO. Hence these logs were not used in training the model
2. Imbalanced classes. Anhydrite, Basement, Chalk, Coal, Dolomite, Halite, Limestone, Marl, and Tuff were underrepresented
REFERENCES
1. https://petrowiki.spe.org/Lithology_and_rock_type_determination
2. https:/github.com/bolgebrygg/Force-2020-Machine-Learning-competition/blob/c8d01ee92c1c8e1ecba36f96cca6ea7b689338a1/lithology_competition/data/train.zip